## Slide 1: Liquid Waste Management in Health Care Facilities
Wastewater Treatment Technologies
Mr. Krishna Ram Yendyo
CEO, EcoConcern Pvt. Ltd.

## Slide 2
WATER BALANCE
RAIN WATER
STORM WATER
CITY SUPPLY/BORING
RAIN
BLACK WATER
GREY WATER
TOXIC WATER
INTRODUCTION:

## Slide 3
WATER BALANCE
RAIN WATER
STORM WATER
CITY SUPPLY/BORING
RAIN
BLACK WATER
GREY WATER
TOXIC WATER
INTRODUCTION:
WASTEWATER

## Slide 4: Characteristics of wastewater
BLACK WATER
High Organic
BOD 200-500
COD 650- 1400
TSS 180 -1000
GREY WATER
Low Organic
BOD 80-150
COD 220-400
TSS 30-170
TOXIC WATER
Photochemical
Disinfectants
Pharmaceuticals
Radioactive waste
Lab chemicals

## Slide 5: Liquid Waste Treatment: Kathmandu Case
14 out of 16 hospitals do not treat their liquid waste before disposal.
hospitals who do ,do not test the treated effluent before disposal
Most hospitals discharge their liquid waste directly into municipal sewerage system without any pretreatment.

## Slide 6: Risks from Health Care Facilities

## Slide 7: Implications
Environmental Implications:
Eutrophication ---- Algal Bloom
chemical & Pharmaceuticals …. Endocrine (or Hormone Disruptors)
Antibiotics – Antibiotic resistant pathogens
Mercury and Heavy Metals

## Slide 8: Implications
Vector-borne Diseases:
Malaria
Encephalitis
Water-borne Diseases:
Cholera
Hepatitis A and E
Typhoid Fever
Diarrhoea
Giardiasis

## Slide 9: Implications
Aesthetics of City
Odour
Ugly Rivers
Absence of Aquatic Animals
Loss of water based recreations
Water Economy
Loss of Water Source
Loss of water Use
Unhealthy farm products
Loss of water civilization

## Slide 10: Treatment Technology
CENTRALISED TREATMENT SYSTEM
DECENTRALIZED TREATMENT SYSTEM
OPD
SURGERY
LAB
Radiology
EMERGENCY
LAUNDRY
WASTEWATER TREATMENT PLANT
OPD
CANTEEN
STAFF QUARTER
LAB
Radiology
WWTP1
WWTP2
LAUNDRY
WWTP3

## Slide 11: Treatment Technology
NATURAL TREATMENT SYSTEM
MECHANISED TREATMENT SYSTEM
Wastewater Treatment Plant for Dhulikhel Hospital
Proposed MBBR wastewater treatment plant for Urban Hospitals

## Slide 12: Treatment Technology: Toxic Wastewater
Acid-Base Neutralization, MBR Treatment Plant, EC Treatment Plant
Electro-Coagulation
Membrane Bioreactor (MBR) Treatment Plant

## Slide 13: Wastewater Reuse in Hospital
Wastewater Segregation
End Use
Treatment Technologies
Greywater
Natural Treatment
Toilet Flushing
Black water
MBBR
Gardening
Toxic water
EC
Public Sewer

## Slide 14: WAY FORWARD
SMART Treatment: Creating Business, Creating Employment, Creating Values
Adding Value to Hospital Management
Minimizing risk to public health
Protection of ambient environment

## Slide 15: Lets treat hospital waste before it pollutes us
THANK YOU
Contact:
Mr. Krishna Ram Yendyo
Krishna.yendyo@ecoconcern.com.np
+977 9841394378
(Wastewater treatment plant design and installation)